## Slide 1: 5.3 Dynamic View(1)
Communication Diagram: registerNode
:NodeManager
registerNode(Serial)
1.2: registerNode(NodeId, ServerInfo, Serial)
1.5: Authenticate
(ESessionKey(NodeId, Serial))
: Note
: Object
: Link
: Asynchronous
: Synchronous or Call
: Reply
1.6: Authenticated
(ESessionKey(Result, ThingList))
1.5: onRegisterEvent
(Result, ThingList)
:UI Controller
1.1: registerNode(NodeId, ServerInfo, Serial)
1.6: onRegisterEvent
(Result, ThingList)
:UI View
:DB
1.6a: [Result=Autorized]
storeThings(ThingList)
1.7: updateRegister
(Result)
Serial is input by User. User can recognize it from SA node’s physically label.
1: registerNode(NodeId, Serial)
Sa-Node verify for security whether serial input from user is the same with SA-Node’s.
1.4: Registered
(EPubKey(NodeId, SessionKey)
1.3: Register(NodeId, ServerInfo, PubKey)
:SA-Node(Arduino)
:Discover
Security
PubKey : IoTMS’s public key. This key is used for sharing SessionKey.
SessionKey : made by SA-Node. This key is used for communicating between SA-Node and IoTMS.

## Slide 2: 5.3 Dynamic View(2)
Communication Diagram: addNode
:NodeManager
:Node
: Note
: Object
: Link
: Asynchronous
: Synchronous or Call
: Reply
:DB
addNode(NodeId, Link)
1: getThingList(NodeId)
:ThingFactory
:Thing
2.1*: [i:=0…ThingsList.size()]
: createThing(Type, Id)
Iteration
Loop to create thing
Create
newly created instance
2: addNode(ThingList, Link)
Create
newly created instance
2.2: create(Type, Id)
Type is used for distinguishing Sensor and Actuator.
addNode is called by Discover when SA-node registered successfully.

## Slide 3: 5.3 Dynamic View(3)
Communication Diagram: controlThing
:NodeManager
:Link
controlThing(selection,value)
:SA-Node(Arduino)
: Note
: Object
: Link
: Asynchronous
: Synchronous or Call
: Reply
:UI Controller
[Result=Success]
1.1a : doCommand(nodeid,thingid,type,value)
:UI View
1: controlThing(nodeid,thingid
,type,value)
Sa-Node
control actuator
:RuleManager
1.1: controlThing(nodeid,thingid
,type,value)
1.1a.1: send(nodeid
,thingid,type,value)
1.1a.2: send(nodeid
,thingid,type,value)
Rule Manager
Check rule sets and decide denial of control
[Result=Deny]
1.1b: deniyAction()
[Result=Deny]
1.1b.1: Result of denial

## Slide 4: 5.3 Dynamic View(4)
Communication Diagram: updateSensorInfo
:NodeManager
:Link
: Note
: Object
: Link
: Asynchronous
: Synchronous or Call
: Reply
:UI Controller
1.1a:[value != thing.prevValue]
UpdateThing(NodeId
,ThingId,value)
:UI View
1: updatelThing(NodeId
,ThingId, value)
:RuleManager
1.1: UpdateThingInfo(nodeid
,thingid,type,value)
1: onData(NodeId
,ThingId,value)
Rule Manager
Check rule sets and decide action-control
1.1a:[value != thing.prevValue]
UpdateThing(NodeId
,ThingId,value)
:SA-Node(Arduino)
updateSensorInfo()
1.1b: [value = thing.prevValue]
No operation
1.1aa: [ruleMatched()=true]
doCommand(nodeid,thingid,type,value)
doCommand
Hereafter start with 1.1a in Communication Diagram of controlThing.
1.1ab: [ruleMatched()=false]
No operation

## Slide 5: 5.3 Dynamic View(5)
Communication Diagram: sensor mal-function
:NodeManager
:Link
: Note
: Object
: Link
: Asynchronous
: Synchronous or Call
: Reply
:UI Controller
1.1a:[value != thing.prevValue]
UpdateThing(NodeId,ThingId,value)
:UI View
1: updatelThing
(NodeId,ThingId, value)
:RuleManager
1.1: UpdateThingInfo(nodeid
,thingid,type,value)
1: onData
(NodeId,ThingId,value)
Rule Manager
Check rule sets and decide sensor mal-function
:SA-Node(Arduino)
updateSensorInfo()
1.1b: [value = thing.prevValue]
No operation
1.1aa: [ruleMatched()=true]
sendMessage(nodeid,thingid,type,value)
sendMessage
Send mal-function message to predefined user.
1.1ab: [ruleMatched()=false]
No operation
:Message
1.1a:[value != thing.prevValue]
UpdateThing(NodeId,ThingId,value)
Mal-function
Rule can handle sensor mal-function.
Condition : predefined senorsor’s upper/ lower boundary
Actions : notify user such as message (default),
* User may change both conditions and actions.

## Slide 6: 5.3 Dynamic View(6)
Communication Diagram: actuator mal-function
:NodeManager
:Link
set mode (alarm)
:SA-Node(Arduino)
: Note
: Object
: Link
: Asynchronous
: Synchronous or Call
: Reply
:UI Controller
[door!=close]
2.2.b : sendMessage (nodeid,thingid,type,value)
:UI View
1: setMode (alarm)
Sa-Node
control actuator
:RuleManager
1.3: send
(nodeid,thingid,type,value)
: close door
1.4: send
(nodeid,thingid,type,value)
: Close door
Rule Manager
Check rule sets and
do predefined actions. (Close door)
:Message
1.1: setMode (alarm)
updateSensorInfo()
2: onData
(NodeId,ThingId,value)
: Door sensor
2.1: UpdateThingInfo
(nodeid,thingid,type,value)
: Door sensor
2.2 UpdateThing
(NodeId,ThingId,value)
: Door sensor
1.2: doCommand
(nodeid,thingid,type,value)
: close door
[door == close]
2.2.a : set Alarm mode

## Slide 7: 5.3 Dynamic View(7)
Sequence Diagram: discoverNode, registerNode

## Slide 8: 5.3 Dynamic View(8)
Sequence Diagram: Connect