## Slide 1: Agenda
Time | Contents | 
15 min. | Presentation | 1. Project overview 2. Architectural driver 3. Perspective view 4. Architectural Design 5. Design & Implementation 6. Wrap up
15 min. | Demo | 1. Add home node 2. Add mailbox node 3. Away mode 4. Secure mode 5. Malfunction mode 6. Add rule 7. Show Log & Remove node
10 min. | Q & A | 
Notes: DBR2 : 센서 / 엑츄에이터 예제 서술
DBR3 : 센서 구조 예제 그림 그리기

## Slide 2: IoT Management System (Initial Presentation)
Team 2

## Slide 3
CONTENTS
  1. Project Overview
  2. Architectural Driver
  3. Architectural Overview
  4. Design & Implementation
  5. Conclusion

## Slide 4: 1. Project Overview
Overview
Our Team is working for an organization that intends to enter the IoT market.
We make an Internet of Things(IoT) system that enables end-users to communicate with sensors and actuators installed in the home or business via PC or smartphone connected to the internet.
(For example, indoor and outdoor light, temp and humidity sensor, door open-close actuator, door open-close sensor, secure alarm, presence/proximity sensor)
Presence
Sensor
Light
Door
Open-Close
Temp.
sensor
Humidity
sensor
Secure Alarm
Arduino
Wi-Fi
router
Notes: DBR2 : 센서 / 엑츄에이터 예제 서술
DBR3 : 센서 구조 예제 그림 그리기

## Slide 5: 2. Architectural Drivers
  2.1. Context
  2.2. Stakeholders
  2.3. Functional Requirements
  2.4. Quality Attributes Utility
  2.5. Constraints

## Slide 6: 2.1 Context - Market, Organizational
Market Context | 
Stakeholders | Customer, End-user, System Installer, Developer
System Access | Users want to access the system via PC, Mobile devices
Functional expectations | After system installation, users expect the system to work automatically by assigned rules of sensors and actuators
Environment | There are many vendors developing a system, sensors and actuators. But there is no standard of interface.
Organizational Context | 
Roles and responsibilities | Project Manager(includes planning, risk and configuration, schedule) Architect Requirement Manager Test Manager Documentation Manager Developer (all members)
Technical background | Digital-Appliance SW solution researcher & developer Smart-phone SW developer Camera module testing SW developer
Notes: DBR4 :Any more assumptions? Such as using commonly found sensors, actuators to reduce cost? Using open source apps. Would the browser be different for mobile devices and PC's :
DBR5 : How about planning manager, risk manager, configuration manager, customer liaison? If you sourced these roles from a framework then which one?
DBR6 : Very broad. Can you be more specific, consumer durable goods, or IT or government products?

## Slide 7: 2.1 Context - Business, Technical
Technical Context | 
Development Skills | Java , C, JavaScript, HTML5
Platforms | Arduino Platform, Laptop Computers
Tools | Eclipse, Arduino IDE
OS | Windows, Linux
HW platform | Arduino , X86
Business Context | 
Date of Delivery | 26 June 2015
Time Resources | 498 man-hours (48+450) :48 man-hours (8 hours X 6 people) in Korea :450 man-hours(3 hours X 6 people X 5 days X 5 weeks) in CMU
Strategy | Easy to use & high extensibility for sensors/actuators
Target Market | B2B - Building Architect Office, B2C - DIY User
Profit Model | Rental Service, Standalone, System Education, Maintenance
Future direction | Many kinds of sensors/actuators(indoor air quality sensor, camera, thermostat controller and so forth) is used & it makes a lot of use case. So big-data of these cases would enable to make services of IoT System.
Notes: DBR7 : May be better to consider hours here instead of 7 weeks. Would that be a better measure of to use for determining what you can get done?
 working day 3hours, Weekend 8hours
DBR8 : Such as? Examples
 센서 : 조도 센서, 거리센서, 컬러 스펙트럼 센서 , 카메라
 actuator : 온도 조절기 , 조도 조절기 , ????
DBR9 : this is good to consider technical risks early.

## Slide 8: 2.2 Stakeholders
Stakeholders of the IoT Management System (IoTMS)
  Customer
  End-User
  System Installer
  Application Developer
  Value-added-resellers (VARs)
  Service Provider
  Maintainer
  Project consultant (or mentor)
Notes: DBR10 : How about project consultant, or mentor too?
DBR 11 : Good, but usually in the US we spell out the acronym first and then in parens give the acronym. As is this is OK

## Slide 9: 2.3 Functional Requirement
Req. ID | Description
FR-12 | The system should make it easy for developers to implement new protocol about new devices.
FR-13 | The system provides user define scenario service like IFTTT(IF This Then That)
FR-14 | When the system sends emergency message, it will be E-mail. In future, it can be SMS or tweet.
FR-15 | When sensors value is abnormal(out of range), the system sends an alarm message to user.
FR-16 | User sets configurations of E-mail address, logging-duration, secure response time and lights waiting time.
FR-17 | The system provides Web APIs for Web developer.
Notes: DBR15 : added by whom

## Slide 10: 2.4 Quality Attributes Utility
QA Type | ID | Description | Priority | Difficulty
Availability | QA-01 | Server recognizes malfunction of sensors within 10 seconds. | High | Medium
 | QA-08 | Detect and notify Logging failure in 30 seconds. | Low | Low
Usability | QA-02 | All function of System is served in 3 depth UI. | Low | Medium
Scalability | QA-03 | IoTMS allow up to 50 SA Nodes. | High | Medium
Modifiability | QA-04 | Emerging new protocol, it is possible to be developed in 2 man-months. | Medium | Medium
Security | QA-05 | IoT Management System allow only authorized user to access in secure way. | High | Medium
Testability | QA-06 | 80% of test cases can be tested within 1 day. | Medium | Medium
Performance | QA-07 | The response time of controlling and monitoring is within 10 seconds. | Medium | High
Modifiability | QA-09 | The System allows to add an new rule without additional development. | Medium | High

## Slide 11: 2.5 Constraints
ID | Description
CST-01 | Schedule Limitation: 7 weeks(include a plan-time in Korea) 498 man-hours (48+450) :48 man-hours (8 hours X 6 people) in Korea :450 man-hours(3 hours X 6 people X 5 days X 5 weeks) in CMU
CST-02 | Human Resources: 6 people
CST-03 | User can’t buy SA nodes and sensors/actuators separately.
Technical Constraints
ID | Description
CST-01 | End-user communicates with sensors/actuators via PC or Smartphone connected to the Internet.
CST-02 | An SA node has 1 or more sensors/actuators.
CST-03 | An SA node uses Wi-Fi communication(802.11)
CST-04 | The IoTMS should be made by Java Language & Arduino device
CST-05 | The IoTMS works on PC or Server
Business Constraints
Notes: DBR21 : As recommend use hours, may be a better granualrity. Weeks implies a work week of 40 hours minimum. Willl you have that much time? DBR22 : Another area where minimum may be better for planning. And it isn't 7 people? Also, are all developers?

## Slide 12: 3. Architectural Design
  3.1. System Context Diagram
  3.2. Allocation view
  3.3. Dynamic view

## Slide 13: 3.1 System Context View
IoTMS
Node
Command :
Door on/off, light on/off,
alarm on/off
- Register node
- Node information for registration
Sensing Data : Temperature/Humidity/Door /Presence(proximity)/Mail Box
: System Element
: Data flow
Log In
Register User
Add, Delete Node
Set Customize rule
Log information
Set Alarm mode (Secure / Unsecure)
Door on/off
- Light on/off
<< Display information >>
User Authorization Success / Fail
Node Authorization Success / Fail
Set Rule Success / Fail
Display Log information
- Node information
: User
: User action(Event) to IoTMS
Legend

## Slide 14: 3.2 Allocation View
http
Web Server
(apache-tomcat-8.0.23)
http
second node
arduino-1.0.6
Database
(mariadb-10.0.19)
IoTMS
Windows 7
http
Port #8080(User)
Web Browser
Mail
box
first node
arduino-1.0.6
Alarm
Temp.
&Humi.
Proxi.
Door
Light
Door
Internet
TCP
Port #3250(Discovery)
TCP
Port #550
(Arduino)
TCP
Port #3250(Discovery)
Sensor
Actuator
node
Arduino
node
User
Machine
IoTMS
Server
Machine
Legend
Data
repository
SW on Machine
Router
11/32
TCP
Port #3250(Discovery)
……..
…..
…..
Senor N
Senor 1
Actuator N
Actuator 1
50th node
arduino-1.0.6
……..
Home PC
Web Browser
Mobile device , office PC

## Slide 15: 3.3 Dynamic Perspective View
12/32
Node
Node Manager
E v e n t B u s + J S O N
User Interface Manager
Message Manager
Log Manager
Communication
Manager
User DB
Log DB
Things object List
A
B
: information, from A to B
DB
Manager
Thing object
(Sensor, actuator...)
Node object
Link object
A
B
: JSON event , from A to B
Node
actuators
actuators
sensors
sensors
Default
sensors
Default
sensors
Rule Manager
Rule DB
confirm
: TCP/IP , from A to B
A
B
SA node (Arduino)
e-mail
twitter
user access
Web UI
message
JSON
thread
reset
kick
Node
Legend
event bus
watchdog
Link
Link
JSON
SA
Home , mail box , …. , 50th node

## Slide 16: 3.3.1 Design Decision – Event Bus w/ JSON
Event Bus | 
Advantage | Disadvantage
Less coupling 2) Provides extensibility 3) Easy to track the interaction between packages | Single point of failure Solution: Recovery Mechanism 2) Performance on heavy duty Solution: Reduce System Load 3) Concurrency Solution: Queuing
Why JSON?
Less coupling Cross platform Human readable UI and SA Node speak the same language UI (Java Script) and database friendly

## Slide 17: 4. Design & Implementation
  4.1. Security
  4.2. Availability
  4.3. Modifiability
  4.4. Scalability & Performance

## Slide 18: 4.1.1 Security – User Management
Framework :
- Spring framework can filter user access with URL Pattern.
- It uses access filter xml, so it applies user access control easily
- should be necessary to study framework.
[Design decision]
In-House :
- If using cookie, It can develop simply.
- But we can apply just web page. According to implementation, it cannot apply at Web API.
- And it is more chance to mistake.
User Access
View
Spring Intercept
URL
Spring validates
Spring displays
View
Spring displays
error message
Spring shows
Login page
User Enter
id & password
[Login successful]
[Login failed]

## Slide 19: 4.1.2 Security – Secure Connection
System 큰 그림
Figure) Secure Node Registration Sequence
Figure) Secure Node Connecting Sequence
Test Environment
Performance Consideration for Arduino RSA 32bit AES 128bit Random Key Generation
SA Node
IoTMS
PubKIoTMS
EPubKIoTMS(SKnode)
Generate
SKnode
ESKnode(SerialNumber)
Decrypt
DSKnode(ESKnode
(SerialNumber))
Decrypt
DPrvKIoTMS(EPubKIoTMS
(SKnode))
ESKnode(Result)
Decrypt
DSKnode(ESKnodeo(Result))
Decrypt
DSKnode(ESKnodeo(Data))
EPubKIoTMS(SKnode)
Generate
SKnode
ESKnode(Result)
Decrypt
DSKnode(ESKnode(Result))
Decrypt
DPrvKIoTMS(EPubKIoTMS(SKnode))
ESKnode(Data)
SA Node
IoTMS

## Slide 20: 4.2.1 Availability – Sensor Malfunction.

## Slide 21: 4.2.2 Availability – Actuator Malfunction.
ㅌ

## Slide 22: 4.3.1 Modifiability - User Defined Rule
if nodeB@temp==Over35#Temperature and nodeA@preseceA==AtHome#Presence
then nodeB@aircon=On@AirConditioner
Rule := if {conditions} then {actions} [condition := {nodeID}@{thingID}=={Value}#{Type}(Delay)?]

## Slide 23: 4.3.2 Modifiability - Support Emerging Protocol
Category | Operation | Parameter | Description
Discovery | discover | duration | Find adjacent SA nodes
 | register | secure key | Register the discovered node
 | unregister |  | Remove the node from the registered list
Link | connect |  | Connect to the node
 | disconnect |  | Disconnect from the node
 | send | data | Send data with JSON format
 | receiver | data | Receive data with JSON format
Figure) Protocol Stacks for SA Nodes
Figure) Structure of Protocol Adapter

## Slide 24: 4.4 Performance Evaluation
http
Web Server
(apache-tomcat-8.0.23)
Database
(mariadb-10.0.19)
IoTMS
Windows 7
http
Port #8080(User)
Web Browser
TCP
Port #550
(Arduino)
node
Arduino
node
Windows
PC
IoTMS
Server
Machine
Legend
Data
repository
SW on Machine
Router
Simulator
TCP
Port #3250~3300
(Discovery)
Simulating 50 SA Nodes
first node
arduino-1.0.6
TCP
Experiment Steps
Run IoTMS Connect a Real SA Node to IoTMS IoTMS send Ping to Real SA Node every 1sec The second PC creates Virtual Nodes made for simulation The second PC makes Node increase 1 per every sec Node sned Thing information to IoTMS every 3sec The second PC makes Node increase until 500ea We measure response of echo from Real SA Node
Environement
  IoTMS : Intel i5 2.7Ghz, 4GB RAM
  2nd PC for 500 virtual SA Node
  SA Node : Arduino

## Slide 25: 4.4 Scalability and Performance
Result of Ping-echo
Node 250
Node 340 (Response > 10s)

## Slide 26: 4.4 Scalability and Performance
How we solve IoTMS overload?
  degrade gracefully
Node
IoTMS
Node
Send information
every 3 sec
Node
IoTMS
Node
Send information
every 6 sec
If Nodes are 250 or more,
Event period change from 3 seconds to 6 seconds

## Slide 27: 4.4 Scalability and Performance
Result of experiment with degradation
Node 250
Node 340 (Response > 10s)

## Slide 28: 5. Wrap up
  5.1. Time Log and Earn Value
  5.2. Role and Responsibility
  5.3. Lessons Learned

## Slide 29: 5.1 Time log & Earn Value
KOREA
CMU
gap C
gap A
gap C
gap A
 Put the more resource to experiment & implementation.
 Long discussion and late decision about architecture design.
gap B
gap B
 Under time estimation about workload.
W1
W2
W3
W4
W5
W6
W7
W8
Plan
Analysis (architecture driver)
Design( system context, perspective view )
Documentation
implementation
System test
Module test

## Slide 30: 5.2 Role & Responsibility
Role | Responsibility |  | Assign
Project Manager | Risk & Issue Management , Schedule Management |  | JONGHYUN HAN
Architect | Requirement Analysis , Architecture Design |  | YOUK KWON
Requirement Manager | Requirement Management |  | JANG YOUNG KEUN
Test Manager | Test Strategy , Test Plan , Test Management |  | DONGOG MIN
Time Log Manager | Time log management , Earned value management |  | JUNG BO HYUN HYUN JIN WOOK
Development | IoTMS | User Interface manager , Log manager , message manager | JONGHYUN HAN
 |  | Rule manager | JUNG BO HYUN
 |  | Node manager | DONGOG MIN
 |  | Communication manager | YOUK KWON
 |  | Event bus + JSON | HYUN JIN WOOK
 | Arduino |  | JANG YOUNG KEUN HYUN JIN WOOK

## Slide 31: 5.3 Future Needs and Lessons Learned
* Future Need
1. Implement adding emerging protocols.(Bluetooth, Zigbee..etc)
2. Implement the encryption (AES, RSA…etc) JSON message between IoTMS and Node.
3. Implement watchdog for single point failure recovery of event bus.
* Lesson Learned
1. Stop discussion, do experiment. - A.J. Lattanze
 Schedule was delayed for a long meeting about design decision.
Arduino memory constraint
 Technical constraint matters.
3. Decoupling is good.
 Because we use the Event bus and JSON, it’s easy to integrate the modules.
4. Manner make the good team work

## Slide 32: Demo Scenario
Login
Add Node
  Discover (SA Node home)
  Register (Serial Number for Security)
Node Event Update
  Door Open by alarm, Turn on the light
Add Node (Mail Box)
Node Event Update (Mail Box)
Away mode
  Send Confirm Message (Tweeter 한책임 Phone)
  Automatic Door Close, Light off
Break-in
  Unknown coming in
  Emergency message (Tweeter)
Malfunction
  Sensor (Pin out )/ Actuator (Door)
Add Rule
  Open door if mail arrives
  Add invalid rule
Remove Node
Notes: DBR2 : 센서 / 엑츄에이터 예제 서술
DBR3 : 센서 구조 예제 그림 그리기

## Slide 33: Questions

## Slide 34: Appendix
Static view of NodeManger

## Slide 35: Appendix
Static view of NodeManger

## Slide 36: Appendix
Static view of NodeManger

## Slide 37: Appendix
Class Diagram of NodeManger

## Slide 38: Appendix
Communication Diagram: addNode
:NodeManager
:Node
: Note
: Object
: Link
: Asynchronous
: Synchronous or Call
: Reply
:DB
addNode(NodeId, Link)
1: getThingList(NodeId)
:ThingFactory
:Thing
2.1*: [i:=0…ThingsList.size()]
: createThing(Type, Id)
Iteration
Loop to create thing
Create
newly created instance
2: addNode(ThingList, Link)
Create
newly created instance
2.2: create(Type, Id)
Type is used for distinguishing Sensor and Actuator.
addNode is called by Discover when SA-node registered successfully.

## Slide 39: Appendix
Communication Diagram: registerNode
:NodeManager
registerNode(Serial)
1.2: registerNode(NodeId, ServerInfo, Serial)
1.5: Authenticate
(ESessionKey(NodeId, Serial))
: Note
: Object
: Link
: Asynchronous
: Synchronous or Call
: Reply
1.6: Authenticated
(ESessionKey(Result, ThingList))
1.5: onRegisterEvent
(Result, ThingList)
:UI Controller
1.1: registerNode(NodeId, ServerInfo, Serial)
1.6: onRegisterEvent
(Result, ThingList)
:UI View
:DB
1.6a: [Result=Autorized]
storeThings(ThingList)
1.7: updateRegister
(Result)
Serial is input by User. User can recognize it from SA node’s physically label.
1: registerNode(NodeId, Serial)
Sa-Node verify for security whether serial input from user is the same with SA-Node’s.
1.4: Registered
(EPubKey(NodeId, SessionKey)
1.3: Register(NodeId, ServerInfo, PubKey)
:SA-Node(Arduino)
:Discover
Security
PubKey : IoTMS’s public key. This key is used for sharing SessionKey.
SessionKey : made by SA-Node. This key is used for communicating between SA-Node and IoTMS.

## Slide 40: Appendix
Communication Diagram: removeNode
:NodeManager
:Node
: Note
: Object
: Link
: Asynchronous
: Synchronous or Call
: Reply
removeNode(NodeId)
:SA-Node(Arduino)
1.1: removeNode()
1: removeNode()
SA-Node return to status waiting for discover when it receive removeNode().
removeNode is called by User.
2: removeNode(NodeID)
This removeNode is removing Node object of NodeManager.
This removeNode is sending remove command and disconnecting Node.